| Spring Weekend 2013 – Dance Hall – Pinky 1 – Phonic 24 |
| --- |
| Channel | Musician/Function | Mic | Band | Notes |
| 1 | Jeff - Keyboard | DI | S |  |
| 2 | Jeff – Bass | DI | S |  |
| 3 | Ashley – Fiddle | XLR for clip-on | S |  |
| 4 | Ashley – Mando | XLR for pickup | S |  |
| 5 | Ryan – Fiddle & Fidola | XLR for clip-on | S |  |
| 6 | Christa – Bodhran | Short boom CM10 | S |  |
| 7 | Christa – Vocal | Tall boom 58 w/sw | S |  |
| 8 | Daron – Fiddle | XLR for clip-on | G |  |
| 9 | Paul – mando, guitar, etc | Short boom C1000 | G |  |
| 10 | Paul – Accordion left | XLR for pickup | G |  |
| 11 | Paul – Accordion right | Short boom SM77 | G |  |
| 12 | Dave – Guitar | DI | G |  |
| 13 | Dave – Upright Piano | pickup | G |  |
| 14 |  |  |  |  |
| 15 |  |  |  |  |
| 16 | Caller Wireless | Shure on T stand |  |  |
| Aux 1 | Band 1 | B212a |  |  |
| Aux 2 | Band 2 | B212a |  |  |
| Aux 3 | Piano monitor | B212a |  |  |
| Aux 4 | Band 4 | B212a |  |  |
| Aux 5 | Ducking |  |  |  |
| Aux 6 | Caller Monitor | AN100 |  | postfader |
| Main L | House Front | B215a x 2 |  | TS99 x 2 |
| Main R | House Rear | B212a x 2 |  | Ledge |
| Mono |  |  |  |  |

Bring clock, no overhang feed, put 212a on ledge at 30 ft facing rear, use shark, bring mixing table, switch cable for lights, b/u power block, 100ft stinger for b/u power